# Trakia Journal of Sciences, Vol.1, No 3, pp  19-22, 2003

# Copyright  © 2003 Trakia University

# Available on line at:

# http://www.uni-sz.bg

## ISSN 1312-1723

#### Review Article

CURRENT STATE OF ANALYTICAL METHODS FOR THE DETECTION OF RESIDUES IN BEE PRODUCTS

St. Bogdanov

Swiss Bee Research Centre, Federal Dairy Research Station, Bern, Switzerland.

#### ABSTRACT

The objective of this paper is to review shortly the current state of the analytical methods, used for the examination of bee products. The principle of different methods is given and the advantages and the shortcomings of each method are discussed. Firstly, there is a focus on the methods, used for determination of the main contaminants in bee products, especially of antibiotics in honey. For determination of  antibiotics the screening methods Charm II Test and ELISA are used. Secondly, all positive samples are determined quantitatively by HPLC, LC-MS. Methods for determination of persistent acaricides and pesticides, as well as for the determination of some volatile contaminants in honey and other bee products, are described and discussed.

Key words: Bee products, Residues, Contamination, Analytical methods, Current status.

The objective of this paper is to review shortly the current state of the analytical methods, used for the examination of bee products, focusing on the main contaminants in bee products. The different methods for the determination of antibiotics in honey are reviewed.

# 1. Antibiotics in honey

Presently antibiotics have been the main contaminants in honey. The following antibiotics have been detected in honey (see Reference list).

- Sulfonamides: sulfathiazole, sulfamethazine, sulfamethaxazole, sulfanilamide

- Aminoglycosides: streptomycine

- Tetacyclines: Oxytetracycline, chlortetracycline

- Amphenicols: Chloramphenicol

The following antibiotics have been reported to be used in apiculture, but there are no published works on their detection:

Beta-lactams (penicillins) and macrolides: tylosine, erythromycin

In routine analysis of honey antibiotics are generally tested by:

- Screening, determination of positive samples: Charm II Test, ELISA

- Quantitative determination of positive samples by HPLC, LC-MS

## Screening methods

### ELISA

Elisa a radio-immuno assay, in which antibiotics are quantitatively assayed by specific antibodies.  It has been tested successfully in honey (1). The detection limit is 10 to 50 ppb. With this method the concentration range of individual antibiotics can be quantitatively determined. Because of cross reactivity with other antibiotics from the same group the method can be used only for semi-quantitative determination. Now this screening method has been largely replaced by the Charm II test.

### Charm II Test

The Charm II test was produced by Charm Sciences Inc. USA. It is a screening test, used for different food as meat and milk, which has been adapted for honey testing. There are published reports on the use of the method (2, 3).  It is based on the specific binding of antibiotics to receptors. The quantitation is determined by measuring of radioactivity: H3 or C14 . The Charm II test can detect the whole group of antibiotics. There are tests for testing in honey of: sulfonamides, tetracyclines, beta-lactams, macrolides, amphenicols and aminoglycosides of the streptomycin type. The screening by the Charm test will exclude the negative samples. The positive samples have to be confirmed by other methods (HPLC, LC-MS, see below). The rate of the correctly classified positive samples depends on the experience of the laboratory. Thus 0 to 30 % of the positively tested samples will be confirmed by other methods. Also, the tests for some antibiotics (e.g. streptomycine) are safer for others (e.g. sulfonamides).It has been found out, that Para Amino Benzoic Acid (PABA), a natural honey constituent, can disturb the test for sulfonamides and yield “false positive” results. Also, there are matrix effects, especially in honeydew and chestnut honey, which lead to an increased rate of “false positive” samples. It seems that the detection level for each antibiotic group depends on the honey type. As a whole, the Charm test for honey is a valuable tool for routine testing for honey producers and packers. Its main advantages are:

- It tests a whole group of antibiotics

- It is considerably cheaper than the other quantitative methods

## Quantitation

The results of the Charm test are qualitative to semi-quantitative. The positively tested samples are further analysed by HPLC and LC-MS methods for quantitation of the residues.

### HPLC

Only the recent literature will be considered, as older methods have detection limits in the ppm determination range. References from earlier literature can be found in  Kaufmann et al. (4). The HPLC is good for routine work, where known antibiotics are analysed. The drawbacks of HPLC are:

- Each antibiotic class has to be tested separately

- There is no 100 % certainty regarding the safe identification of the antibiotics

Recently automatic HPLC systems which include sample extraction and HPLC determination have been developed (http://www.applica-analytik.de). This is a promising development, aiming at a less labour intensive and cheaper antibiotic determination.

Sulfonamides are bound to honey sugars. That is why an acid hydrolysis step is included in the method. The sulfonamides are derivatised for fluorimetric detection and afer  separation by reversed-phase HPLC are detected by Diode Array Detector or by a fluorescence detector (5, 6). The limit of detection is about 5 ppb, the limit of quantitation lies at 10-15 ppb, the recoveries of 11 different substances vary from 70 to 100 %.

Streptomycin is analysed by reversed-phase HPLC, followed by post-column derivatisation to enable fluorescence detection (2, 7,  8). The limit of detection is about 5 ppb, the limit of quantitation is 10 ppb.

###### Tetracycline and oxytetracycline were determined by reversed-phase HPLC with UV detection in a study of the degradation in honey, but the limit of detection was quite high, about 1 ppm (9). Oxytetracyline (terramycine) degrades within 5- 9 weeks (9, 10) into different metabolites (9). In a recent ring trial, conducted by FAPAS (11) different HPLC methods with fluorescence detection have used, the detection limit being about 50 ppb (4,12). The residue level of 0.6 ppm chlortetracycline tested in this collaborative study was far above the levels, expected in the praxis.

### LC/MS-MS

This is the most modern and promising method. The analysis is based on clean up by SPE, separation by reversed-phase HPLC and subsequent detection by MS-MS. The MS-MS insures an almost “100 %-safe” specific detection with a very low background noise. The method was developed by Kaufmann et al. (13) for sulfonamides, tetracyclines (tetracyclines, oxytetracycline and chloroxytetracyclines) and flumequine. The limit of detection is 0.5 to 10 ppb, depending on the substance. The method is being presently extended to include also chloramphenicol and streptomycine. The objective is the development of a LC/MS-MS method, capable of detecting all antibiotic residues in honey.

# 2. Acaricides and pesticides

## 2.1. Acaricides and pesticides in honey

A list of the recent methods used is given below. Both GC and HPLC methods have been used. GC methods with MS detection seem to be most promising.

### Gas Chromatography

In most cases the techniques use extraction of honey by SPE or organic solvents, followed by separation on capillary chromatography with ECD, NPD or MS detection. For methods for the detection of the most commonly used acaricides and pesticides see the reference list below. The limit of determination lies between 1 and 10 ppb. The limit of detection of thymol lies at about 0.02 ppm, the limit of determination being around 0.1 mg/kg (14).

### HPLC

Reversed-phase HPLC with Photo Diode Array Detection is successfully used. The determination limit for synthetic acaricides is higher than the one achieved by GC methods and lies typically between 10 and 50 ppb. The limit of detection of organic acids lies at about 1 ppm.

### Enzyme analysis

A combined determination of oxalic and formic acid can be carried out with the Boerhinger Kit, Germany (15). Oxalic acid can also be determined with a Sigma Kit (16). The limit of detection of these methods lies between 3 and 5 ppm.

## 2.2. Acaricides and propolis in beeswax

The method, mostly used for the determination of the most common acaricdes bromopropylate, coumphos, fluvalinate and flumethirne is: extraction by hexane, separation from high-molecular compound by freezing centrifugation, purification on Florisil columns and subsequent determination by capillary GC and ECD detection (17, 18). The detection limit is 0.1-0.25 ppm. The objective is to enlarge the deermination scope by including other varroacides as amitraz, cymiazole etc, as proposed by Korta et al. (19). Only GC-MS detection will allow the detection of all acaricides, used for varroa control.

# 3. Volatile contaminants

Volatile contaminants can be tested with head-space or SPME techniques (20, 21, 22):

- Repulsive substances used in honey harvest (phenol, nitrobenzene)

- Anti-wax moth substances: para-dichlorbenzene, naphthalene

- Components of essential oils: thymol

# 4. Quality assurance

The introduction of Quality Assurance in analytical laboratories according to the EN 45001 and ISO 9000 norms allow precise and reproducible measurements of trace amounts of residues in bee products. Collaborative trials should be regularly carried out to ensure good performance of the testing laboratories. Three collaborative trials have been carried out recently with bee products : suflonamides in honey, tetracycline in honey and acaricides in beeswax (see reference list).

# References

- Heering, W., Usleber, E., Dietrich, R., Märtlbauer, E., Immunochemical screening for antimicrobial drug residues in commercial honey, The Analyst 123: 2759-2762, 1998.

- Kocher, U., Nachweis von Streptomycin-Rückständen in Honig mittels Charm II-Test und Absicherung der Befunde durch HPLC mit Nachsäulenderivatisierung und Fluorescenzdetektion,Lebensmittelchemie 50: 115-117, 1996.

- Edder, P., Corvi, C., Utilisation du Charm II pour le dépistage des résidus d'antibiotiques dans les denrées alimentaires d'origine animale, Mitt.Lebensm.Hyg. 92 : 218-228, 2001.

- Kaufmann, A., Pacciarelli, B, Prijic, A., Ryser, B., Roth, S.,  Bestimmung von Rückständen von Tetracyclinen in Lebensmitteln, Mitt.Lebensm:Hay. 90: 167-176, 1999.

- 5. Schwaiger, I., Schuch, R., Bound sulfathiazole residues in honey - Need of a hydrolysis step for the analytical determination of total sulfathiazole content in honey, Deutsche Lebensmittel   Rundschau 96: 93-98, 2000.

- Diserens, J.M., and Savoy-Perroud, MC., (2002)  Determination of sulfonamaide residues in honey, Report of the NRC Nestle Research center, 1000 Lausanne 26, Switzerland.

- Klementz, D., Pestemer, W., (1996) Extraktion, clean-up und HPLC - Bestimmung von streptomycin in Apfel-, Honig- und Nektarproben. - erste ergebnisse aus freilandversuchen., Nachrichtenblatt des Deutschen Pflanzenschutzdienstes 48: 280-284.

- Edder, P., Cominoli, A., Corvi, C.,  Dosage de résidus de streptomycine dans le miel par HPLC avec postdérivatisation et détection fluorimétrique, Mitteilungen aus dem Gebiete der Lebensmitteluntersuchung und Hygiene 89, 369-382, 1998.

- Sporns, P., Kwan, S., Roth, L.A., HPLA analysis of oxytetracycline residue in honey, J. Food. Prot. 49: 383-388, 1986.

- Argauer, R.J., Moats, W.A.,  Degradation of oxytetracycline in honey as measured by fluorescence and liquid chromatographic assays, Apidologie 22, 109-115, 1991.

- Knaggs, M., Powell, J., FAPAS (FOOD ANALYSIS PERFORMANCE ASSESSEMENT SCHEME), Honey analysis, report No 2802, Ring trial: determination of tetracycline in honey, 2002.

- Iwaki, K, Okomura, N, Yamazaki, M., Determination of tetracycline antibiotics by reversed-phase high-performance liquid chromatography with fluorescence detection. J.Chromatography, 623: 153-158, 1992.

- Kaufmann, A., Roth S., Ryser, B., Widmer M., Quantitative LC-MS-MS determination of sulfonamides and some other antibiotics in honey, Journal of AOAC International 85: 853-860, 2001.

- Bogdanov, S., Kilchenmann, V., Imdorf, A., Acaricide residues in some bee products, Journal of Apicultural Research 37, 57-67, 1998.

- Bogdanov, S., Charriere, J.D., Imdorf, A., Kilchenmann, V., Fluri, P., Determination of residues in honey after treatments with formic and oxalic acid under field conditions, Apidologie 33, 399-409, 2002.

- Mutinelli, F., Baggio, A., Capolongo, F., Piro, R., Prandin, L., Biaison, L., A scientific note on oxalic acid by topical application for the control of varroosis, Apidologie 28: 461-462.

- Zimmermann, S., Gierschner, K.H., Vorwohl G., Bestimmung von Brompropylat, 4,4-Dibrombenzophenon, Coumaphos und Fluvalinat, Bienenwachs Deutsche Lebensmittel-Rundschau 89: 341-343, 1993.

- Bogdanov, S., Imdorf, A., Kilchenmann, V., Residues in wax and honey after Apilife VAR treatment, Apidologie 29, 513-524, 1988.

- Korta, E., Bakkali, A., Berrueta, L.A., Gallo, B., Vicente, F., Study of an accelerated solvent extraction procedure for the determination of acaricide residues in honey by high-performance liquid chromatography-diode array detector, Journal of Food Protection, 65: 161-166, 2002.

- Conte, L., Bortolomeazzi, R., Moret, S., Sabatini, A., Marcazzan, G., Applicazione della microestrazione in fase solida (spme) alla determinazione del fenolo nei mieli, J. of Food Science and Nutrition 26, 97-102, 1997.

- Volante, M., Cattaneo, M., Bianchi, M., Zoccola G., Some applications of solid phase micro extraction (SPME) in the analysis of pesticide residues in food, Journal of Environmental Science and Health, Part B - Pesticides, Food Contaminants and Agricultural Wastes 33, 279-292, 1998.

- Piasenzotto, L., Gracco, L., Conte, L. Bogdanov S., Application of Solid Phase Microextraction to Evaluate Traces of Thymol in Honey, Apidologie, 2002 (in print).

# Footnotes

* Correspondence to: Stefan Bogdanov,  Liebefeld, Schwarzenburgstrasse 155, CH-3003 Bern, Switzerland, Tel:	+41(0)31 323 82 08,

Fax: +41(0)31 323 26 02,

E-mail: stefan.bogdanov@fam.admin.ch http://www.apis.admin.ch